Operations and Readiness Division						    14 April 2004

MEMORANDUM FOR Waterways Association of Pittsburgh

SUBJECT:  April 2004 Meeting

##### REPORT ON LOCK CLOSURES AND DELAYS TO NAVIGATION

1.  The following is the schedule of lock closures and delays to navigation interests through

30 June 2004.

Locks & Dam 2, Monongahela River -  A contractor for the U.S. Army Corps of Engineers is removing the existing fixed crest dam at Mile 11.2; this demolition work began in late March 2004 and should take about 60 days to remove the existing fixed crest dam.  River traffic passing the site should not be interrupted with the exception of periodic delays just prior to and immediately following any scheduled blast.  These delays may occur as often as once per day during the main demolition phases of this work and the delays will last 1.5 to 2 hours.  Scheduled blasting is expected to occur sometime between noon and 4:00 PM.  Now that the old fixed crest dam is breached, the new gated dam at Braddock will maintain the upstream pool at Elevation 721.8 (upper gage of 12.1) which will provide a vertical clearance of 42.5 feet under the Conrail Railroad Bridge at Mile 11.7, Monongahela River.  (Reference Notice to Navigation Interests No. 04-13)

Locks & Dam 4, Monongahela River -  The U.S. Army Corps of Engineers demolition contractor at Lock 4 (Charleroi) removed the small 56ft x 360ft lock chamber from operation on 12 April 2004.  Thus the large 56ft x 720ft lock chamber is the only means to transit Charleroi until construction of the new 84ft x 720ft river chamber is completed in the next 10-12 years.  River conditions permitting, plans call for a second 24-hour shutdown from 8:00 AM on 19 April thru 8:00 AM on 20 April 2004.  A contractor will also be constructing pivot and protection cells in the upstream lock approach at Charleroi.  It is anticipated that this work will begin within the next week and 2-hour delays to river traffic will occur periodically during the cell construction work.  The contractor, River Salvage Company, will have an assist/helper boat available during construction of the cells.  All river traffic will need to transit the lock slowly using extreme caution.  (Reference Notice to Navigation Interests No. 04-16)

Morgantown L/D, Monongahela River -  The U.S. Army Corps of Engineers Repair Fleet will replace the land wall filling valve and renovate its operating machinery in the single 84ft x 600ft lock chamber.  Work is scheduled to begin on 20 April 2004 and continue thru 30 April 2004.  Intermittent delays up to 4 hours may be encountered during this 11-day work period.  (Reference Notice to Navigation Interests No. 04-19)

Opekiska L/D, Monongahela River -  The U.S. Army Corps of Engineers Repair Fleet will close and dewater the single 84ft x 600ft lock chamber to repair the lock gates, sills, and floating mooring bitts.  Work is scheduled to begin on 3 May 2004 and be completed by 27 May 2004.  No river traffic will be able to pass through the lock during this 25-day work period.  (Reference Notice to Navigation Interests No. 04-18)

2.  The following Internet sites are recommended for the most up-to-date navigation information:

a. Daily Navigation Conditions:

http://www.lrd-wc.usace.army.mil/text/pitrpti.txt

b. Current River Conditions:

http://wmw.lrp.usace.army.mil/current/

c. Pittsburgh District Navigation Notices:            http://www.lrp.usace.army.mil/or/navrpt.htm

d. Braddock Web Cameras:

http://www.lrp.usace.army.mil/webcam/braddock_webcam.htm

3.  Morgantown L/D, Hildebrand L/D and Opekiska L/D on the upper Monongahela River

will operate on the following schedule beginning in April 2004.  Morgantown will be open from 7:00 AM to 3:00 PM Monday thru Friday; and from 12:30 PM to 8:20 PM on Saturdays, Sundays and Holidays from April through the month of November 2004.  Appointment lockages at Morgantown will be accepted from commercial tows after hours (during the non-operating hours).  Hildebrand and Opekiska will be open from 12:30 PM to 8:20 PM on Saturdays, Sundays & Holidays from April thru November 2004.  Appointment lockages at Hildebrand and Opekiska will be accepted from commercial tows after hours except during the period from 11:00 PM to 6:30 AM each day.  (Reference Notice to Navigation Interests No. 04-15)

/s/

RICHARD C. LOCKWOOD

Chief, Operations and Readiness

Division

2

RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. Of Pittsburgh  Meeting 04/14/04

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--www.erh.noaa.gov/pit

WEATHER RECAP

Precipitation was near normal in the Monongahela and Ohio  River basins averaging 3.25 – 3.75 inches. In the Allegheny River Basin precipitation averaged about 3.00 inches or 0.50 of an inch below normal.

At the Pittsburgh International Airport monthly precipitation was 3.60 inches which was 0.43 of an inch above normal. Temperature averaged 2.9 degrees/day above normal. Monthly snowfall was 8.6 inches bringing the seasonal total to 53.5 inches. Normal snowfall for the season is 40.6 inches

For the first 13 days of April temperatures have been 4.6 degrees/day below normal, precipitation was 2.70 inches or 1.40  of an inch above normal. There were 0.5 inches of snow bringing the seasonal total to 54.00 inches or 14 inches above normal.

RIVER FLOWS

Rivers were at near to slightly below normal levels at the beginning of March. Temperatures averaging 15 to 25 degrees above normal produced significant snow melt and rivers began rising during the first week of March.  The snowmelt was followed by heavy rains over the Monongahela River Basin.  The Monongahela River rose 7 – 13 feet on 6 - 7 March with a subsequent rise of 6 – 8 feet on the Ohio River. Elizabeth Locks and Dam crested at 20.0 feet on 7 March. Flood stage is 20 ft. Rivers generally receded over the next two weeks, but a warm rainy period during the last 10 days of the month produced a rise on the Allegheny River when the remainder of the snow pack melted.

Heavy rains of 2-3" during the past two days have resulted in 6 – 12 foot rises and minor flooding (1' above flood stage) at Connellsville on the Youghiogheny River, and at Charleroi and Elizabeth on the Monongahela River. Rainfall of 1-2" elsewhere caused river rises of 2-3" on the Allegheny and 6-12 feet on the Ohio. Pittsburgh is expected to crest at around 22.8 feet this afternoon. All rivers are forecast to recede to near normal levels during the next 3-4 days.

HIGH WATER POTENTIAL

High water potential is currently above normal on the all rivers in the region.  Rivers flows are above normal, groundwater levels are high, and soils remain saturated. After they recede over the next few days, a widespread 1 – 1.5 inches of rain in 12 to 24 hours is needed to bring the major rivers back up to bank full.

WEATHER FORECAST

Today: Light Rain. High 48.

Tonight: Partly Cloudy. Low 30.

Thursday: Mostly Sunny. High 58.

Thursday Night: Clear. Low 35.

Friday: Partly Sunny. High 68.

Friday Night: Partly Cloudy. Low 48.

Saturday: Partly Sunny. High 70.

Saturday Night: Partly Cloudy. Low 50.

Sunday: Partly Sunny. High 72.

Monday: Chance of Showers. High 65. Low 45.

Tuesday: Partly Cloudy. High 60.

The 8 to 14 day forecast is for above normal temperature and near normal precipitation.

The April Outlook is for near normal temperatures and precipitation.

The May-Jun-Jul Outlook is for near normal temperature and precipitation.