Operations and Readiness Division						    18 February 2004

MEMORANDUM FOR Waterways Association of Pittsburgh

SUBJECT:  February 2004 Meeting

##### REPORT ON LOCK CLOSURES AND DELAYS TO NAVIGATION

1.  The following is the schedule of lock closures and delays to navigation interests through

30 April 2004.

Hildebrand L/D, Monongahela River -  A contractor for the U.S. Army Corps of Engineers is continuing to perform maintenance dredging, river and weather conditions permitting.  The dredging should be complete by the end of March 2004.  Only minor delays to navigation are expected.  (Reference Notice to Navigation Interest No. 04-02)

Dashields L/D, Ohio River -  The U.S. Army Corps of Engineers Repair Fleet will renovate the middle wall filling and emptying valves and their operating machinery in the 110ft x 600ft lock chamber.  Work is scheduled to begin on 2 March 2004 and will be complete by 23 March 2004.  The 56ft x 360ft river lock chamber will be closed to navigation traffic during the work period.  The 110ft x 600ft land chamber will remain open with only intermittent delays expected.  (Reference Notice to Navigation Interests No. 04-03)

Dashields L/D, Ohio River -  The U.S. Army Corps of Engineers Repair Fleet will repair the upstream land wall gate damaged in a navigation accident starting on 23 March 2004 and continuing thru 26 March 2004.  The 110ft x 600ft lock chamber will be closed to navigation during this 4-day work period.  The 56ft x 360ft lock chamber will be open for river traffic.  The Corps coordinated the lockage procedures with the Waterways Association before issuing the navigation notice for this job.  (Reference Notice to Navigation Interests No. 04-04)

Hildebrand L/D, Monongahela River -  The emergency bulkhead for the upstream end of the single 84ft x 600 ft lock chamber needs to be inspected and repaired which will require the lock chamber to be closed to river traffic.  This work is scheduled from 8:00AM thru 4:00PM on 13 April 2004.  The inspection and repairs to the emergency bulkhead are necessary in order to be prepared for the upcoming dewatering job at Hildebrand in May 2004.  (Reference Notice to Navigation Interests No. 04-09)

Morgantown L/D, Monongahela River -  The U.S. Army Corps of Engineers Repair Fleet will replace the land wall filling valve and renovate its operating machinery in the single 84ft x 600ft lock chamber.  Work is scheduled to begin on 19 April 2004 and continue thru 29 April 2004.  Intermittent delays up to 4 hours may be encountered during this 11-day work period.  (Reference Notice to Navigation Interests No. 04-05)

Locks 2 and Locks 3, Monongahela River -  Navigation accidents have resulted in damage to upstream lock gates in the land chamber at both projects as well as damage to the guidewall and light pole at Locks 3.  Repairs are anticipated to be completed during the 5–16 April 2004 time period.  Lock chamber closures for these repair jobs are expected to have minimal impact to river traffic; more details will follow in Notices to Navigation Interests.

2.  The following Internet sites are recommended for the most up-to-date navigation information:

a. Daily Navigation Conditions:

http://www.lrd-wc.usace.army.mil/text/pitrpti.txt

b. Current River Conditions:

http://wmw.lrp.usace.army.mil/current/

c. Pittsburgh District Navigation Notices:            http://www.lrp.usace.army.mil/or/navrpt.htm

3.  The U.S. Army Corps of Engineers demolition contractor at Charleroi anticipates that in the May 2004 timeframe, the small 56ft x 360ft lock chamber will be taken out of operation.  Thus the large 56ft x 720ft lock chamber will be the only means to transit Charleroi until construction of the new 84ft x 720ft river chamber is completed in the next 10-12 years.

/s/

RICHARD C. LOCKWOOD

Chief, Operations and Readiness

Division

RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. Of Pittsburgh  Meeting 02/18/04

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--www.erh.noaa.gov/pit

WEATHER RECAP

Precipitation averaged about 3.5 inches in the Allegheny and Monongahela River basins or 0.50 - 0.75 of an inch above normal. In the Ohio River basin precipitation averaged about 4.00 inches or 1.00 - 1.5 inches above normal.  Statewide, 2003 was the second wettest year in the last 108 years with an average precipitation of 53.45 inches.

At the Pittsburgh International Airport monthly precipitation was 4.78 inches which was 2.08 inches above normal. Temperature averaged 5.3 degrees/day below normal. Monthly snowfall was 18.3 inches bringing the seasonal total through January to 40.8 inches. Normal snowfall through the end of January is 22.7 inches.

For the first 17 days of February temperatures have been 1.2 degrees/day below normal, precipitation was 2.16 inches or 0.78 of an inch above normal. There were 2.1 inches of snow bringing the seasonal total to 42.9 inches.

RIVER FLOWS and ICE

Rivers began to rise on 2 January due to snow melt with temperatures averaging 20 to 25 degrees/day above normal. Heavy rains totaling of 2.0 - 3.0 inches moved across east central Ohio, the upper Ohio River Valley, and the lower Allegheny and Monongahela River basins on 3-4 January.  Minor flooding also occurred on the Ohio River at Moundsville. In addition, the Ohio River crested within a half foot of flood stage at Pike Island Lock and Dam, Wheeling, and Powhatan Point. The Allegheny River rose 3 - 5 feet and the Monongahela River 7-12 feet between 2-5 Jan, but crested below flood stage.

Flows were already above normal preceding the heavy rain and snow melt event during the first few days of January.  All rivers crested by 6 Jan and receded throughout the remainder of the month. By the end of January flows were generally at or slightly below the long term median flows for late January. The Allegheny River below  Lock 3 is ice free, Locks 3&4 40-50% ice covered (3-6 in), and 100% coverage (6-12 in) from Locks 5-9. The Ohio and Monongahela Rivers are ice free.

HIGH WATER POTENTIAL

High water potential is normal on the all rivers in the region.  Rivers flows are about 50% of normal,  groundwater levels are high, soils are frozen, ice is limited to the upper Allegheny River with no major jams, and the deep snow pack is becoming limited to the upper Allegheny basin (SD 12/ SWE 3) and the higher terrain of the Cheat basin (SD 12/SWE 3-4).  A widespread 2.0 to 2.5 inches of rain and snowmelt in 12 to 24 hours is needed to bring the major rivers to bank full.

WEATHER FORECAST

Today: Sunny. High near 40.

Tonight: Partly cloudy. Low near 30.

Thursday: Partly cloudy. High in the lower 40s.

Thursday Night: Partly cloudy. Low around 30.

Friday: Mostly cloudy with a 30 percent chance of rain showers. High in the upper 40s.

Friday Night: Mostly cloudy with a 50 percent chance of rain showers. Low near 35.

Saturday: A 60 percent chance of rain. High near 45.

Saturday Night:  40 percent chance of rain showers..changing to snow showers after midnight. Low near 30.

Sunday: Partly cloudy. Low 25 to 30. High in the upper 30s.

Monday: Partly cloudy. Low 25 to 30. High in the upper 30s.

Tuesday: Partly cloudy. Low 25 to 30. High in the upper 30s.

The 8 to 14 day forecast is for near  normal temperature and below normal precipitation

The February Outlook is for near normal temperatures and precipitation.

The Mar-Apr-May Outlook is for near normal temperature and precipitation