U.S. Army Corps of Engineers, Pittsburgh                                                            February 9, 2011

Operations Division

MEMORANDUM FOR WATERWAYS ASSOCIATION OF PITTSBURGH

SUBJECT: February, 2011 Meeting

##### ITEMS OF INTEREST TO NAVIGATION

- LOCK CLOSURES AND DELAYS

The Pittsburgh District’s work at Pike Island L/D is finally complete. Although traffic moved well and the delays to navigation were all manageable, the Corps of Engineers would like to express our thanks to Towing Industry for the exceptional cooperation and patience which they exhibited throughout this extended work period.

The first scheduled work for next year, by the Repair Fleet is from 16 March to 15 April, 2010, at New Cumberland L/D.  This work will be to replace two Filling or Emptying valves and will entail a closure of the small chamber.  The main chamber will remain operational and only slight delays to navigation should be expected.

We may need to alter our maintenance schedule further for FY-11, to accommodate cost overrides for Pike Island.  If the need does occur, we will coordinate with the Navigation Committee, in order to address industry’s needs.

The ice conditions have subsided on all area rivers, except the Allegheny. We will no longer be sending out a morning ice report, unless conditions worsen.  The ice in the Allegheny remains mild and stationary with little change.   All locks are open for traffic.

2.  RECOMMENDED INTERNET SITES - The following sites are recommended for the most up-to-date navigation information.

a. Daily Navigation Conditions:  www.lrd-wc.usace.army.mil/text/pitrpti.txt

b. Current River Conditions:  http://wmw.lrp.usace.army.mil

c. District Navigation Notices:  www.lrp.usace.army.mil/or/or-f/navrpt.htm

3. OTHER ITEMS OF INTEREST

Walsh Construction, Contractor for Pennsylvania Turnpike will be constructing a four-lane concrete box girder bridge supported by two river piers constructed from causeways, over the Monongahela River at about Mile 59.1 near Denbo (Vesta No. 6), Washington County, Pennsylvania.  Navigational clearance during construction will be about 345 feet.  The work will be performed from 7:00 a.m. to 5:00 p.m. Monday through Friday beginning Monday, March 2, 2009 and ending February 7, 2011.  During this work, the M/V Okan Express provided by Ed McGavin would move the 40-foot x 50-foot, 7-foot draft Shugart Barge floating plant mounting a Reed SK 35 truck-mounted drill rig. The plant will include an 18-foot Skiff boat for safety.

Notice is hereby given that the USACE – Pittsburgh District will no longer send Notices to Navigation Interests by e-mail.  In order to view these notices, you must access the USACE – Pittsburgh District web page at www.lrp.usace.army.mil/or/or-f/navrpt.htm.

USACE will continue to send electronic version of Notices to Navigation Interests to USCG (United States Coast Guard) and the Waterways Association.

/signed/

RICHARD C. LOCKWOOD

Chief, Operations Division

# RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. of Pittsburgh Meeting 02/09/11

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--http://www.weather.gov/pittsburgh

## WEATHER RECAP

The only significant rainfall was on 1 Jan when up to 0.75 of an inch of rain fell on portions of western Pennsylvania and northern West Virginia. During the remainder of the month precipitation was generally snow with liquid equivalent less than 0.50 of an inch per day.  There was measurable snow on 18 days in January, and there has been snow on the ground in Pittsburgh since January 6th.

At the Pittsburgh International Airport monthly precipitation was 2.41 inches, which is 0.29 of an inch below normal. Temperature averaged 3.4 degrees/day below normal. Snowfall in January was 24.1inches or 11.8 inches above normal.

For the first 8 days of February temperatures were normal and precipitation was 1.12 inches which is 0.48 of an inch above normal.  There has been 3.9 inches of snowfall in February bringing the total seasonal snowfall to 40.2 inches, or 15.0 inches above normal.

### RIVER FLOWS and ICE

The most significant river rise of the month occurred from 1-3 January.  Rises were 3-6 feet on the Allegheny and Ohio Rivers and 2-4 feet on the Monongahela River.  Rivers generally receded for the remainder of January. For the month flows averaged near normal on the Allegheny River basin and below normal on the Monongahela and Ohio River basins. Significant amounts of ice are limited to the upper portion of the Allegheny River, but will be increasing across the region through Friday.

#### HIGH WATER POTENTIAL

The high water potential is near normal. Currently flows are 60-70% of normal on the Allegheny River, 125-150% of normal on the Monongahela River, and near normal on Ohio River.  Rainfall and/or snowmelt of 1.5 – 2.0 inches in 6-12 hours are needed to bring rivers to bank full. Deep snowpack is limited to the upper Allegheny basin and higher terrain of Cheat and Yough basins with snow depths of 12-18 inches and snow water equivalents of 3.0 - 4.5 inches.

##### WEATHER FORECAST

Today…Partly Sunny. High near 25

Tonight…Partly cloudy. Low zero to 5 above.

Thursday…Sunny. High in the mid teens

Thursday night…Clear and cold. Low 5 to 10 above.

Friday…Mostly sunny. High near 30.

Friday night…Mostly cloudy. Low around 20.

Saturday… Mostly cloudy with scattered flurries. High in the lower 30s.

Saturday Night… Mostly cloudy with scattered flurries. High in the upper 20s.

Sunday… Mostly cloudy with scattered flurries. High in the mid to upper 30s.

Monday…40% chance of rain showers. Low in the upper 20s. High in the lower 40s.

Tuesday…Mostly cloudy with flurries. Low in the upper 20s. High in the mid 30s

8-14 Day Outlook…near normal temperature precipitation.

Feb Outlook...below normal temperature and above normal precipitation.

Mar-Apr-May Outlook…near normal temperature and precipitation.