U.S. Army Corps of Engineers, Pittsburgh                                                       10 January 2007

Operations Division

MEMORANDUM FOR Waterways Association of Pittsburgh

SUBJECT:  January 2007 Meeting

##### ITEMS OF INTEREST TO NAVIGATION

1.  LOCK CLOSURES AND DELAYS - The following is the schedule of lock closures and delays through 31 March 2007.

Montgomery Dam, Ohio River Update-   A navigation accident on 18 October 2006 resulted in dam gate #8 being knocked from its hoisting chains completely destroying it and dam gate #4 being severely damaged.  Gravity dams have been installed in gate bay #8 and in gate bay #4.  Both gravity dams have been anchored to reinforce the dams against ice loading and high water overtopping.  The gravity dams are closing off the flow through each gate bay until new dam lift gates can be procured and installed.  Technical Support Division completed plans and specifications for the fabrication and installation of new dam gates to replace gates #4 and #8.  Request for proposal W911WN-07-R-0002 has been issued to the public for the New Gates Replacement at Montgomery Locks and Dam.  The Request for Proposal package has been released through the FedTeDS website.  A pre-bid meeting was held at Montgomery L/D on 20 December 2006 and numerous contractors attended.  Date to receive offers is 18 January 2007.  This is a negotiated procurement, not an invitation for bid, so there will be no public bid opening.  The Corps will award to the lowest price, technically acceptable offeror.

The Repair Fleet is replacing deteriorated structural members and riveted connections on 3 dam lift gates.  The repairs to #6 and #5 dam lift gates have been completed and both gates are fully operational.  The emergency/maintenance bulkheads were moved from gate bay #5 to gate bay

#2 on 22 December 2006.  The Repair Fleet continues to replace deteriorated structural members and riveted connections on dam gate #2.  High water conditions have temporarily halted work on #2 lift gate; it is anticipated that work will resume next week and repairs will be completed by 31 January 2007.  This repair work on the 3 dam gates is not related to the navigation accident.

There is currently no unrestricted flow on the dam.  With the maintenance bulkheads set in gate bay #2 and the 2 gravity dams in place in gate bays #4 and #8, we have capability to operate the other 7 dam lift gates to control pool levels up to 70-feet of dam opening.

C.W. Bill Young L/D, Allegheny River-  The U.S. Army Corps of Engineers Repair Fleet will repair the Land Wall 8' x 10' Filling Valve in the single 56-ft x 360-ft lock chamber and repair deteriorated segments of hydraulic pipeline at the lock.  The repair work is scheduled to begin 12 March 2007 and is expected to be complete by 30 March 2007.  The lock chamber will be open to navigation during this work period; however, closures of 4 to 8-hours will occur periodically (approximately 6 times during the 19-day work period) to move and install valve parts and equipment on the land wall; and also during the replacement of hydraulic pipeline segments.

SUBJECT:  January 2007 Meeting                                                               10 January 2007

2.  RECOMMENDED INTERNET SITES - The following sites are recommended for the most up-to-date navigation information.

a. Daily Navigation Conditions:  www.lrd-wc.usace.army.mil/text/pitrpti.txt

b. Current River Conditions:  http://wmw.lrp.usace.army.mil

c. District Navigation Notices:  www.lrp.usace.army.mil/or/or-f/navrpt.htm

3.  OTHER ITEMS OF INTEREST

- Navigation Notice 07-1 containing the planned schedule of lock maintenance work during calendar years 2007 and 2008 was issued on 5 January 2007 after meeting with representatives of the Waterways Association.

/s/   James J. Rockovich

for RICHARD C. LOCKWOOD

Chief, Operations Division

2

# RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. Of Pittsburgh Meeting 1/10/07

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--http://www.weather.gov/pittsburgh

## WEATHER RECAP

Temperature was much above normal in December, and rainfall was below normal.  There were three rain events in the 0.5 to -.75 of an inch range that resulted in minor rises on the major rivers in the region. Rainfall averaged about 2.00 inches across the region or 0.75 - 1.25 inches below normal.

At the Pittsburgh International Airport monthly precipitation was 2.01 inches, which is 0.85 of an inch below normal. Temperature averaged 6.3 degrees/day above normal. Snowfall for December was 0.7 of an inch or 6.2 inches below normal.

For the first 9 days of January temperatures were 13.9 degrees/day above normal and rainfall was 1.05 inches or 0.24 of an inch above normal.  The total precipitation for 2006 was 34.92 inches which is 2.93 inches below normal. Snowfall for the winter season is 1.1 which is 12.8 inches below normal.

### RIVER FLOWS

At the beginning of December seven day average flows were near normal throughout the region.  A storm on 1 December produced 0.50 -0.75 of an inch of rain in most areas and rises of 1 – 3 feet on the Allegheny and Monongahela Rivers and 2 - 4 feet on the Ohio River. Back to back rain falls of 0.50 – 0.75 of an inch on 22 and 25 December combined to bring rises of 2 - 4 feet on area rivers between 22 and 28 December. By the end of the month rivers had fallen to near normal levels.

#### HIGH WATER POTENTIAL

The high water potential is near normal. Flows are 350 percent of normal on the Allegheny River, 275 percent of normal on the Ohio River, and 200 percent of normal Monongahela River. There is no significant snow pack or river ice. A widespread 1.5 to 2.0 inches of rain in 6 to 12 hours will to bring rivers to bankfull.

##### WEATHER FORECAST

Today:  Mostly cloudy with scattered flurries. High in the lower 30s.

Tonight: Partly cloudy. Low near 20.

Thursday: Mostly sunny. High in the upper 40s.

Thursday Night: Increasing cloudiness.  Low near 35.

Friday: 40% chance of afternoon showers. High in the upper 40s

Friday night:  70% chance of showers. Low near 40.

Saturday:  70% chance of showers. High in the lower 50s.

Saturday Night: 50% chance of showers. Low in the upper 30s.

Sunday: 60% chance of showers. High in the  lower 50s

Monday: Rain likely. Low near 40. High in the upper 40s

Tuesday:  colder with a chance of snow showers. Low near 25. High in the upper 20s

8-14 Day Outlook…near normal temperature and precipitation.

Jan Outlook...above normal temperature and near normal flows.

Jan-Feb-Mar Outlook… above normal temperature and near flows in the Allegheny and Ohio River basins and below normal in the Monongahela River basin.