U.S. Army Corps of Engineers, Pittsburgh                                                         12 November 2008

Operations Division

MEMORANDUM FOR WATERWAYS ASSOCIATION OF PITTSBURGH

SUBJECT:  November 2008 Meeting

##### ITEMS OF INTEREST TO NAVIGATION

1.  LOCK CLOSURES AND DELAYS - The following is the schedule of lock closures and delays through 31 December 2008.

Dashields L/D, Ohio River - The U.S. Army Corps of Engineers is in the middle of a six-day closure of the main 110-ft x 600-ft lock chamber from 8:00 AM, 10 November 2008 to 11:00 PM, 15 November 2008 to repair the upstream middle wall miter gate that was damaged in a recent allision. It will be necessary to lift the gate out of the water to make the necessary repairs.  During this 6 day repair and closure period all traffic will be routed through the auxiliary 56-ft x 360-ft lock chamber.  The main lock chamber will reopen to navigation at 11:00 PM on 15 November 2008.  Following the reopening of the main lock the auxiliary lock chamber will be closed at 1:00 AM on 16 November 2008 to make repairs to miter gate and valve operating machinery.  The auxiliary lock will remain closed until the completion of this repair work, scheduled for 11:00PM on 18 Novembers 2008. The average delay has been 1 hour and 36 minutes per boat and as of 0700 today there was no queue waiting.

2.  RECOMMENDED INTERNET SITES - The following sites are recommended for the most up-to-date navigation information.

a.   Daily Navigation Conditions:  www.lrd-wc.usace.army.mil/text/pitrpti.txt

b.   Current River Conditions:  http://wmw.lrp.usace.army.mil

c.   District Navigation Notices:  www.lrp.usace.army.mil/or/or-f/navrpt.htm

3.  OTHER ITEMS OF INTEREST

Events – A meeting with the Waterways Association of Pittsburgh is scheduled for 25 November 2008 at PEWARS to discuss the 2009/2010 repair jobs that will have an impact on river traffic.  A draft repair schedule was provided to the WAPgh for review prior to the meeting.

Lock & Dam 6, Allegheny - A contractor for the U.S. Army, Corps of Engineers will be making repairs to the Dam.  This emergency work is due to severe erosion discovered during a recent dive inspection.  Repair work is scheduled to start on or about 17 November 2008 and should be completed by the end of December.  There will be a temporarily drawn down of the upper pool by the hydropower project to assist in the repair work.  A boating safety zone has been established at Dam 6 to keep vessels a safe distance away from the dam until the repair work is completed.  This zone is approximately 1000 feet upstream of the dam and is marked by a line of “Danger Dam” buoys.

Beginning January 2009 the Pittsburgh District’s Notices to Navigation Interests will only be available by email and downloading from the Pittsburgh District webpage at www.lrp.usace.army.mil/or/or-f/navrpt.htm.

/Signed/

RICHARD C. LOCKWOOD

Chief, Operations Division

# RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. of Pittsburgh Meeting 11/12/08

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--http://www.weather.gov/pittsburgh

## WEATHER RECAP

October was slightly cooler than normal and continued the below normal precipitation trend that began in July. There were 12 days with measurable precipitation at the Pittsburgh International Airport, but it was generally very light.  There were only two days with more than 0.25 of an inch of rain. The driest conditions in the region continued to be in the upper Monongahela River basin.  Average precipitation in the Monongahela River basin was about 1.5 inches which is 1.5 inches below normal.  In the Allegheny and, Ohio River basins precipitation averaged 1.75  - 2.00 inches or about 0.75 of an inch below normal.

At the Pittsburgh International Airport monthly precipitation was 2.01 inches, which is 0.24 of an inch below normal. Temperature averaged 1.4 degrees/day below normal

For the first 11 days of November temperatures were 4.0 degrees/day above normal and precipitation was 0.13 of an inch which is 0.90 of an inch below normal.  Precipitation since 1 January is 33.12 inches or 0.12 inches above normal.  PA DEP has issued a Drought Watch for all of Western Pennsylvania.

### RIVER FLOWS

Overall, flows averaged near normal in the Ohio and Muskingum River basins in October. Flows were at or below in the Allegheny and Monongahela River basins with much below normal flows in the Tygart, Cheat and upper Youghiogheny River basins. There were no significant rises on any of the major rivers. For the most part, the main stem rivers fluctuated within a 0.5 to 1.0 foot range.

#### HIGH WATER POTENTIAL

The high water potential is below normal. In the Upper Monongahela River basin flows are 15 – 20% of normal and 35% of normal in the lower Mon.  Flows on the Allegheny River are 45-50% of normal and 35% of normal on the Ohio River. A widespread 2.5 to 3.0 inches of rain in 6 to 12 hours will bring rivers to bankfull.

##### WEATHER FORECAST

Today…Cloudy. High in the lower 50s

Tonight…70% chance of rain after midnight. Low near 45.

Thursday…90% chance of rain. High near 55.

Thursday night…Cloudy. 30% chance of evening showers. Low near 50.

Friday…Cloudy. 40% chance of showers. High in the upper 50s.

Friday night…60% chance of showers. Low near 45.

Saturday…50% chance of showers. High near 45.

Saturday night…40% chance of rain and snow showers. Low in the lower 30s.

Sunday …Cloudy. 40% chance of snow showers. High In the upper 30s.

Monday…Mostly cloudy Low near 32. High in the upper 30s.

Tuesday…40 percent chance of snow showers. Low. Near 35. High near 35

8-14 Day Outlook…below normal temperature and near normal precipitation.

Nov Outlook...near normal temperature and below normal flows

Dec-Jan-Feb Outlook…Below normal temperature and near normal flows